## Slide 1: Update
Accelerating Spark
  Or, using in-network compute to accelerate data analytics

## Slide 2: WHY
Spark is CPU-bound

## Slide 3: WHY
Spark is CPU-bound
Opportunities for relieving CPU
  Assisting sorting
CPU Breakdown for Sort (Map + Shuffle + Reduce)
Sorting

## Slide 4: WHY
Spark is CPU-bound
Opportunities for relieving CPU
  Assisting sorting
  Serialiazation
CPU Breakdown for Shuffle
Serializing data

## Slide 5: LITERATURE
On-the-side accelerators
  GPU, FPGA
  Seen some papers (from earlier in the decade)
On-path accelerators – data filtering
  Switches
  NICs

## Slide 6: LITERATURE
On-the-side accelerators
  GPU, FPGA
  Seen some papers (from earlier in the decade)
On-path accelerators – data filtering
  Switches – two approaches
  NICs – haven’t seen any so far

## Slide 7: SWITCH-BASED
Key idea: Filter data earlier in the data processing so that later (CPU) computation doesn’t get as much work
Limited support for operators like:
  PROJECT
  TOP N
  DISTINCT
  JOIN

## Slide 8: Jumpgate
Where to filter data?
  Disaggregated design
  Closer to storage (before data reaches workers)
Talked to the author from UBC
  Thanks, Stew!

## Slide 9: CHEETAH
Where to filter data?
  Traditional design
  Between master and workers
  CPU savings mostly at master during query processing

## Slide 10: CHEETAH
Where to filter data?
  Traditional design
  Between master and workers
  CPU savings mostly at master during query processing
  Limitations
  Very limited flexibility – only simple queries
  Zero integration – separate master/workers

## Slide 11: Can NICs HELP?
On-path, like switches
  but more flexible
  Allows for better integration and complex queries
Attached to the host, like on-the-side accelerators
  Can enable custom workload acceleration & data placement
Best of both worlds?

## Slide 12: NEXt
Reading some earlier papers that use on-the-side accelerators
  Hasn’t really picked up back then with database engines
  possibly due to data movement overhead across PCIe
Also, is Spark the platform of choice for data analytics or is there something else?

## Slide 13: MISC

## Slide 14: SmartNIC benefits
Picking on FLOEM and NICA…
(Nothing personal!)

## Slide 15: Floem KVS
Compares CPU-only and “CPU+Caching on NIC”
  Shows caching benefits
  Which does worse at <50% hitrate
Benefits from:
  Caching speedup – Yes
  Kernel overheads/netstack – No
  Additional resources – Yes
  NIC acceleration for caching – Unlikely
Confident that on-CPU caching will have similar benefits.

## Slide 16: NICA KVS
Compares CPU-only and “CPU+Caching on NIC”
  Shows caching benefits
  Which does worse at <50% hitrate
Benefits from:
  Caching speedup – Yes
  Kernel overheads/netstack – No
  Additional resources – Yes
  NIC acceleration for caching – likely
Confident that on-CPU caching will have similar benefits.

## Slide 17: SmartNIC benefits
Both works point out KV-Direct as inspiration for KVS offload (and we point to Floem in FairNIC)
  But they take wrong things to offload
  KV-Direct uses caching only to overcome it’s PCIe bottleneck, which is unlikely to happen in hybrid Host-NIC KVS apps.
Would be good exercise to prove this… but what then?
  At least hands-on FPGA experience is tempting..