## Slide 1: ACCELERATING SPARK
Spark is CPU-bound
Opportunities for relieving CPU
  Serialiazation
  Other computation around Shuffle
CPU Breakdown for Shuffle
Serializing data

## Slide 2: SERIALIZATION in SPARK

## Slide 3: ACCELERATING SPARK
Serialization – 8%
Deserialization – 6%

## Slide 4: CEREAL vs SMARTNIC
On-chip Co-processor:
  Min Latency communication
  Exploit all available DRAM bandwidth
  Similar DRAM latency – No data transfer across PCIe
  Easier time integrating with existing framework
With PCIe-based accelerator, you cannot afford to make multiple DRAM accesses.

## Slide 5: WITH NIC: APPROACH?
Gather all the pieces of an object (and its sub-objects) using DMA
  And put them together on the NIC
  Similarly on the receive side…
  Scatter-gather DMA?
  Might avoid some aspects of serialization altogether
How does NIC know where the pieces are?

## Slide 6: WITH NIC: CHALLENGES
Virtual to physical/IO address mapping
  Again, Use CPU’s help?
Socket-based interface no longer works
  Need an app-specific Host-NIC communication interface – RDMA++
  An opportunity for enabling NIC-offloaded operators as well
Doing this with Java might be non-trivial
  Looking at SparkRDMA effort
Spark-architectural challenges
  Spark serializes objects during the map phase and stores them to disk…

## Slide 7: NEXT
Thinking further about the challenges
Going thru the implementation of both Spark and a Java Serializer
  Apache Giraph as well
May be setup SparkRDMA…

## Slide 8: CEREAL vs SMARTNIC
Virtual address space access
  TLB & Faults
  1GB Hugepages
DMA thru PCIe
  How flexible is it?
  Is there enough bandwidth i.e., TPS.
  Cannot do writebacks
Cannot work with traditional interfaces
  Use CPU to list all references and use scatter-gather DMA?
  Avoid serdes altogether…
  A new interface could help with in-network programming too…

## Slide 9: The APPROACH FOR NICs
Explore off-path (PCIe) acceleration solutions (e.g., FPGA-based).
Morphing these to NICs.
  Closer-to-network computation – like shuffle
  Avoid two-way communication across PCIe
  Other factors ?

## Slide 10: Other H/W BASED SERDES
Other works (based in SSD): Morpheus, HODS
Narrow definition of serialization
  Text (Ascii) => Int, Float
  Basically Int.Parse() and Float.Parse() engines
  Marginal speedups
  One on embedded core, other on FPGAs
  Does not apply in our case… but could be an interesting use-case for SmartNICs

## Slide 11: JAVA OBJECT LAYOUT
Header
  Type
  Hash code
  Length
Data
  Values
  References