## Slide 1: Update
RDMA Memory Registration
  Does it all happen in the control path?
  Does RDMA provide the flexibility of registering any memory?
  What’s the cost?
    Where’s the protection domain crossing?

## Slide 2: RDMA reg_mr
APP
KERNEL
RDMA NIC
libibverbs
uverbs
mlnx4
ioctl
read,
write, etc.

## Slide 3: RDMA reg_mr
Control path
Reg_mr(virt_addr, size)
User-kernel switch
Pin physical pages
DMA map the pages (get IOVAs)
  IOMMU on/off?
Communicate with the NIC, which caches it in TLB
Return mr handle
APP
KERNEL
RDMA NIC
libibverbs
uverbs
mlnx4
ioctl
read,
write, etc.

## Slide 4: RDMA reg_mr in datapath
Copy into pre-registered buffer
vs
register memory in datapath
Can register every piece of data – but cancels benefits of RDMA
Amortize reg_mr call with batching?
Is that enough?

## Slide 5: Misc

## Slide 6: rIOMMU
Breaking down the cost of map and unmap operations.
DMA access

## Slide 7: rIOMMU
Breaking down the cost of map and unmap operations.
DMA unmap

## Slide 8: rIOMMU
Breaking down the cost of map and unmap operations.
DMA unmap

## Slide 9: rIOMMU
Breaking down the cost of map and unmap operations.
Cost of mapping dwarfs the cost of translation
These prices are paid on every packet and that’s how it is in Linux => Another reason why DPDK performs so well!

## Slide 10: rIOMMU
Breaking down the cost of map and unmap operations.
Cost of mapping dwarfs the cost of translation
These prices are paid on every packet and that’s how it is in Linux => Another reason why DPDK performs so well!

## Slide 11: RDMA: Memory registration
Does it all happen as control path?
Does RDMA provide the flexibility of registering any memory?
  Tracing jVerbs for an answer
What’s the cost?
  Where’s the protection domain crossing?

## Slide 12: jVerbs
Wrapper around native RDMA calls
Uses off-heap because of direct buffers and access to virtual addresses
RDMA-Core libs

## Slide 13: Next
Learn more about RDMA Memory Registration
5G talk